## Slide 1: The ALICE TPC Upgrade Project
R. Majka
Richard Majka

## Slide 2
What is a TPC and why is it used in ALICE?*
A large cylindrical gas volume with electric field arranged to drift ionization electrons from charged particles passing through the gas to either end.
A magnetic field parallel to the electric field bends the particles and allows measurement of the particle momentum.
By measuring the number of ionization electrons per unit path length for a charged particle the velocity of the particle is determined and one can determine the particle mass.
Invented by Dave Nygren, ~1975 http://www.slac.stanford.edu/pubs/slacreports/reports04/slac-r-190.pdf, p 126
Physics Today 31, 46 (1978); http://doi.org/10.1063/1.2994775

## Slide 3
ALICE TPC
At low momentum the ionization cross section falls with increasing momentum, at higher energy relativistic contraction/dilation of the particle’s electric field causes the ionization cross section to increase.
PEP4 TPC

## Slide 4: Basic idea of gas detector for ionizing radiation:
Ionizing radiation – such as a charged particle –
passing through a gas (usually a noble gas with “additives”) can knock electrons off the gas atoms.
Under the influence of an electric field the electrons can drift to an electrode to be detected.
But, on average only a few ionization electrons/mm are produced. With modern, low noise, inexpensive preamplifiers you need ~ 104 electrons to be comfortably above the noise level.
A mechanism to multiply the signal is needed.
Multiplier
E field
Collection electrode

## Slide 5
Since its invention in 1968 by Georges Charpak*, the basic “workhorse” of gas detectors for tracking high-energy charged particles has been the Multi- Wire Proportional Chamber and its derivatives.
Micro electronics made possible readout for 104 – 105 channels.
* G. Charpak, et al., Nucl. Intrum. and Meth., 62, 262, 1968.
Few mm
1 - 2 mm
 = 25 - 50 m
Field is high enough near wires to accelerate electrons to sufficient energy so they can create further ionization
~2kV – 4kV Many M

## Slide 6: Upgrade of LHC injector chain - What and When
Pb-Pb interaction rate: 8 kHz
50 kHz

## Slide 7
LHC Upgrade → New Physics Opportunities for ALICE
Study the thermalization of partons in the QGP, with focus on
charm and beauty quarks at low pT
  secondary vertices
Low-momentum charmonia dissociation (and regeneration?) to study deconfinement and medium temperature
Production of thermal photons and low-mass dileptons emitted by QGP to study initial temperature and equation of state of the medium
  exploit low pT reach & PID of ALICE
Processes Cannot be selected at trigger level
Move from 1 kHz triggered running in ALICE to 50 kHz Pb-Pb
Record Everything!

## Slide 8: Why We Need to Upgrade the TPC
Present TPC: Wire chamber end plates
p Resolution: spT/pT < 3.5% at pT = 50 GeV/c and below 1% at pT = 1 GeV/c.
•
•
dE/dx resolution: 5% (p-p) – 6.5% (central Pb-Pb) (158 max. samples)
Event rate: 1 kHz Pb-Pb minimum bias
Want to be able to record 50 kHz Pb-Pb collision rate and maintain the current performance
BUT
Drift time for ionization electrons from central electrode to end plate is O (100 s)
Drift time for ions from end plate to central electrode is O (160 ms)
Build up of positive ions in the drift volume → electric field distortion → distortion of the ionization electron tracks as they drift to the end plates
Ions produced by charged particles traversing the detector are unavoidable – this is the signal
Ions from the gain structure - typically a few thousand times the initial ionization -
must be prevented from getting to main drift volume
~

## Slide 9
Main Drift
Gating Grid
Ground Plane Anode wires (gain)
Read out (pad plane)
When a trigger occurs, gating grid is biased (opened) to allow passage of charged particles
The grid is kept open for the time required to collect the ionization electrons O (100 s)
In this time, no ions from the gain element (anode wires) can escape the gain region
Grid then must be kept closed long enough to collect all ions O (300 s)
Intrinsic dead time → rate limitation ~ 3 kHz
Eliminate the gating grid by exploiting the low Ion Back Flow (IBF) of Gas Electron Multipliers (GEMs)*
*B. Ketzer et al., Nucl.Instrum.Meth. A732 (2013) 237-240
Use a gating grid between the gain element and the drift volume
Gating grid is normally biased to prevent passage of charged particles (ionization electrons and ions)
TPC is run in triggered mode
Usual Solution

## Slide 10: Gas Electron Multipliers (GEMs)
140
m
One of several micropattern gas detectors developed over the past ~20 years.
Invented by Fabio Sauli at CERN
Sauli NIM A386(1997)531
1e- in
>103 e-s out
Electric field in the holes ~100kV/cm
70 m
50 m
50 m polyimide
5 m Copper
5 m Copper
Typical parameters:
50m Kapton
metal coated
Ø50-70m holes
• 100-200m pitch
10

## Slide 11
Several year R&D program developed a solution with 4-GEM chambers
Different GEM hole patterns on each GEM helps to block ion backflow
Tradeoff between energy resolution (large gain in first foil) and ion back
flow (IBF) (small gain in first foil)
Standard Pitch not rotated
Large Pitch
rotated
Large Pitch not rotated
Standard Pitch rotated
55Fe peak s/mean (%)
Ion Backflow current / Anode Current (%)
Eight voltages (DV on 4 GEMs and DV on 4 gaps) makes huge parameter space to scan
Curves of energy resolution vs ion backflow show a region that meets our design goals and a larger region that gives acceptable performance to meet the physics goals.
Calibration method for correcting space-charge distortions is already in use for the current run and handles variations even larger than we see in prototype chamber.
90-10-5 Ne-CO2-N2
400 V/cm drift field
DV=270 V
DV=800 V
DV=230 V
DV=359 V
DV=288 V
DV=20
DV=800 V
DV=800 V
Solution – Technology Choice
dE/dx res. =8.5%
dE/dx res. =8.0%
11

## Slide 12: Readout Chamber Design and Construction
ALICE TPC end plate readout is divided into 18 20o sectors on each end. Each sector has an inner chamber (IROC) and outer chamber (OROC). To maintain reasonable sizes for the GEM foils the OROCs are divided into 3 sections.
GEM foil sizes
GEM foil numbers
₋ 40 sectors (36 installed + 4 spare)
₋ 4 GEM stacks per sector
₋ 4 GEM foils per stack
= 640 GEM foils
To accomplish this very large construction effort the project has been divided among several institutions

## Slide 13
Division of Effort for ROC and Electronics Construction and Testing
Managing material flow among many institutes is not a small part of the project. For ROC construction Database is used to track material location, status and archive QA+test data.
45 Institutes

## Slide 14: Division of effort and material flow for ROC construction and testing.
Managing material flow is not a small part of the project.
Database is in place and being used to track material location, status and archive QA+test data.

## Slide 15: Single Foil Advanced QA
Two institutes have optical scanners and software to measure all inner (polyimide) and outer (copper) hole diameters.
We also can map the gain across single foils.
Training neural net software to predict the gain based on optical measurements.
Clear correlation is seen and the optical scan is faster and easier to do.
Every foil will be optically scanned and acceptance criteria established.
Relative Gain
Hole Diameter (mm)
Scan shown is from “flawed” foil – useful to have larger range of hole sizes for neural net training

## Slide 16
Foil Handling and Testing
Commercial stencil stretching frame used. The inner frame is used for handling foils until they are glued onto fiberglass frame.
Foil mounted in inner frame as soon as it comes from CERN shop
Stays with foil until foil is finally trimmed to final fiberglass frame
Outer (blue) frame clamps inner frame and applies calibrated stretching force (Calibrated springs)
HV Testing:
Plexiglass box can be flushed with dry nitrogen.
Spring pins in lid connect to each of the foil HV segments
Multichannel floating pico ammeter developed can measure leakage currents at HV down to a few pA
Foils checked before leaving CERN, at advanced QA site, before and after framing and before mounting in chamber

## Slide 17: Frame in gluing fixture at Wayne State

## Slide 18: Foil in gluing fixture

## Slide 19: Curing in dry atmosphere

## Slide 20
Foil trimming plate
Glass plate with hole matching alignment hole in corner of GEM foil and frame.
Dowel pins keep foil, frame and protective aluminum cover in place during trimming
20

## Slide 21
Alubody at Yale, mounted on base plate for test and shipping vessel

## Slide 22
Close up showing high voltage connectors and cooling tubes

## Slide 24
For assembly work, soldering HV leads to GEM’s or when not necessary to have GEM exposed it is always kept covered.

## Slide 25
IROC foils assembled on pad plane, alubody, test vessel base plate.
Ready for test vessel cover.

## Slide 26
X-ray generator mounted to illuminate full chamber

## Slide 27
Shorting cards bring current from all read out pads to a current meter.

## Slide 28
X-ray Generator
Thin Window
X-Y Stages
X-ray generator mounted to scan chamber to map gain and ion back flow.

## Slide 29: Typical live display while scanning chamber gain vs position

## Slide 30
Assembled Chamber Testing and QA
30
Gas tightness (monitor H20, O2 in gas exit stream)
Gain curve and gain at standard voltages (55Fe peak)
Stability – run for 2 days, monitor gain and any discharges
Spatial map of gain and Ion Back Flow (IBF) – scan chamber with collimated X-ray source, measure anode and cathode currents at each location
“Stress” test – illuminate full chamber with X-ray source to give 10 nA/cm2 anode current (max. expected in operation at LHC). Monitor for discharges.
Inches
Inches
Inches
Inches
*Local IBF variation can be tolerated if the pattern is stable in time. Tests indicate that it is.

## Slide 31: Data Compression
Storage
Reconstruction Compression Monitoring Calibration
50 kHz
75 GB/s
 PEAK OUTPUT
(20 GB/s average)
3.2 TByte/s into PC farm
O2 (Online Offline) System Hardware and software developments ongoing
All this data pouring out of the front end has to be further compressed, monitored, used to feed calibrations back into compression, …

## Slide 32
Status and Schedule
Two full prototype IROC and OROC chambers have been built using nearly final design and tested
Changes made to design and to procedures
Final-design parts ordered for 5 IROC and 5 OROC chambers
Gain more experience before starting full production
Final design chamber built and under test now.
→
→
→
→

## Slide 33
Backup Slides

## Slide 34
New Front End Card (FEC) for TPC Upgrade readout - 5 x 105 Channels
Uses five ALICE custom-designed 32 channel ASICs (SAMPA) providing preamp/shaper/ADC and digital signal processing
3276 FECs will be installed, each with 160 channels using radiation tolerant components (rad tolerant to 5.6 kRad integrated dose)
System continuously digitizes signals at 5 MHz* for 0.5 M TPC channels.
FECs send digitized data over fiber optic links to ALICE Common Readout Units (CRU)
*Detailed simulations show that the TPC sampling rate can be lowered from the present 10 MHz to 5 MHz without compromising the physics performance.
>> Onboard front end zero suppression not required
Baseline correction and zero suppression can be done in a computer – much easier to program and change if needed.

## Slide 35
SAMPA – Custom ASIC for TPC and Muon Tracking Chambers
SAMPA = 32 channel chip – mixed analog and digital – also used for muon tracker upgrade Development plan allows 3 cycles
Cycle 1 – functionality divided into 3 chips, lots of test features included
Cycle 2 – all functions integrated into one chip
  Delivered and tested. Noise performance looks very good - average 360 electrons on the bench
  Some glitches in digital part found but workarounds have allowed functional front end cards (FEC) to be built
  Test
Cycle 3 – all fixes incorporated
Submit this Spring
Expect chips in Summer
Work already ongoing for final FEC design
Test fully instrumented chamber

## Slide 36
TPC Front End Card Prototype (Rev. 0a)
5 cycle 2 SAMPA chips
4 connectors for flat jumpers to connectors on pad plane
Note: Final FEC will be rigid-flex with a flex layer extending here to plug directly into pad plane connectors – no jumper cables needed
18.4 cm
18.6 cm

## Slide 37: Summary The ALICE collaboration is building a major upgrade for the ALICE TPC to be installed in the LHC Long Shutdown 2 (2019-2020)
This upgrade will allow operation in the high luminosity in LHC runs 3 and 4 (50 kHz Pb-Pb collision rate) while maintaining the current physics performance of the TPC.
The upgrade involves:
Replacing all readout wire chambers with quadruple-GEM chambers.
The GEMs are designed to minimize ion back flow to allow continuous, ungated and untriggered readout.
Replacing the front end electronics with electronics based on a new ASIC (SAMPA) designed to allow continuous readout
Developing software to achieve compression of the 3.2 TB/sec raw data from the TPC
This upgrade will allow ALICE to record the full Pb-Pb luminosity and gather very high statistics data sets even for processes where a trigger is not possible.

## Slide 38: Using roller to apply epoxy

## Slide 39: Pressure plate and SS bricks

## Slide 40
FEC Block diagram
40

## Slide 41
What will ALICE do to exploit these new physics opportunities?
This Presentation
Next Presentation, Paolo Martinengo
The new Fast Interaction Trigger detector for the ALICE Upgrade Wladyslaw Henryk Trzaska, Poster
Prospects for ALICE physics with the Muon Spectrometer Upgrade
and the new Muon Forward Tracker
Antonio Uras, Poster
Detector Control System of the new Muon Forward Tracker at ALICE Kenta Shigaki, Poster

## Slide 42
Nygren, http://www.slac.stanford.edu/pubs/slacreport s/reports04/slac-r-190.pdf, p 126