## Slide 1
ALICE Time Projection Chamber (TPC) Upgrade
The Large Hadron Collider at CERN will be upgraded to increase the Pb-Pb ion collision rate from 8 kHz to 50 kHz.
The main charged particle tracking detector at ALICE is a large TPC.
Trails of ionization electrons produced by charged particles passing through the TPC volume are drifted to the endcaps where the signal is multiplied by multi-wire proportional chambers (MPWC) and the transverse position is recorded. The drift time gives the third coordinate and the ionization density can be used to determine the type of particle.
The MWPC chambers will not operate at the projected Pb ion collision rates of 50,000/second – each producing thousands of charged particles.
An upgrade to the TPC will replace the MPWC readout chambers with newer technology Gas Electron Multiplier (GEM) chambers.
New readout electronics
will allow recording of every
collision

## Slide 2: Gas Electron Multipliers (GEMs) - Solution for High Rate Operation
140
m
One of several micropattern gas detectors developed over the past ~20 years.
Invented by Fabio Sauli at CERN
Sauli NIM A386(1997)531
Ionization electrons are guided by the electric field into the holes in the GEM foil where the very high field causes an avalanche – thus multiplying the signal.
1e- in
>103 e-s out
Electric field in the holes ~100kV/cm
70 m
50 m
50 m polyimide
5 m Copper
5 m Copper
Typical parameters:
50m Kapton
metal coated
Ø50-70m holes
• 100-200m pitch

## Slide 3
ALICE TPC end plate readout is divided into 18 20o sectors on each end. Each sector has an inner chamber (IROC) and outer chamber (OROC). To maintain reasonable sizes for the GEM foils the OROCs are divided into 3 sections.
GEM foil sizes
GEM foil numbers
₋ 40 sectors (36 installed + 4 spare)
₋ 4 GEM stacks per sector
₋ 4 GEM foils per stack
= 640 GEM foils
To accomplish this very large construction effort the project has been divided among several institutions
US Teams with DOE support are building the IROCs
46.7 cm
49.7 cm

## Slide 4
Aluminum base fabricated at University of Texas, Austin
Also, vessels for testing and shipping IROCs to CERN.
Pad plane with readout electrodes, Spacer,
High voltage feedthroughs and cooling tube for electronics assembled on aluminum base and tested at University of Tennessee, Knoxville.
Fiberglass frames to support GEM foils fabricated and glued to foils at Wayne State University. Foils tested at high voltage before and after framing.
Final assembly of GEM foils onto chamber body and QA tests with sources and X-ray generator at Yale University
X-ray Generator
Thin Window
X-Y Stages