## Slide 1: EIC Detector R&D
Thomas Ullrich
EIC User Meeting
ANL
July 9, 2016

## Slide 2: 2010/2011 - EIC Key Years
  Last LRP (2007) had good words for an EIC but no recommendation
    “An EIC with polarized beams has been embraced by the U.S. nuclear science community as embodying the vision for reaching the next QCD frontier.”
    “We recommend the allocation of resources to develop accelerator and detector technology necessary to lay the foundation for a polarized Electron-Ion Collider.”
  No funding efforts of DOE for detector R&D
  Fall 2010 INT Workshop “Gluons and the quark sea at high energies distributions, polarization, tomography”
    551 page writeup in August 2011

## Slide 3: 2010/2011 - EIC Key Years
  Work on the EIC White Paper started
    Working groups of few enthusiast
  Few experimentalists from universities involved (although many were interested)
  No organized user group in sight
  Machine design at JLAB and BNL well underway
  No detector design(s) nor R&D efforts
2010/2011 the need to get
the ball rolling was apparent

## Slide 4: Generic Detector R&D for an EIC
In January 2011 BNL, in association with JLab and the DOE Office of NP, announced a generic detector R&D program to address the scientific requirements for measurements at a future EIC
Goals of Effort
Enable successful design and timely implementation of an EIC experimental program
Develop instrumentation solutions that meet realistic cost expectations
Stimulate the formation of user collaborations to design and build experiments
Peer-Reviewed program established in 2011 to enable EIC experiments
Initiator, driver, and coordinator until 2014: Tom Ludlam

## Slide 5: Generic Detector R&D for an EIC
  Funded by DOE, managed by BNL: 1M$-1.5M$/year
  Program explicitly open to international participation
  Key to success: Standing EIC Detector Advisory Committee consisting of internationally recognized experts in detector technology and collider physics
    Meets twice a year
      ~January: Review of ongoing projects
      ~July: Review and new proposals
Current: Marcel Demarteau* (ANL), Carl Haber (LBNL), Peter Krizan (Ljubljana),
Ian Shipsey (Oxford), Rick Van Berg (UPenn), Jerry Va’vra (SLAC), Glenn Young (JLab)
Retired:
Robert Klanner (Hamburg),
Howard Wieman (LBL)

## Slide 6: Consortia
Committee was and is supporting the formation of consortia
  Combining efforts of groups from universities and labs with similar targets
    encourage close collaboration
    sharing of resources, some freedom in distribution of funds
  Currently:
    Tracking consortium - 7 institutions
    Calorimeter consortium - 12 institutions
    PID consortium - 20 institutions
  Potential future candidates:
    Si Vertex consortium
    Software and Computing consortium
First step toward building scientific collaborations to successfully build EIC detector components

## Slide 7: Reminder: EIC Detector Requirements
  -3.5 < η < 3.5 is sufficient for the central detector
    try to get to η = -4 if possible
  Material budget of ≲ 5% X/X0
  Momentum resolution on a (few) % level is fine
    no need to do better at a cost of higher X/X0
  Electron ID
    -3.5 < η < 1; π suppression up to 1:104
    ~2%/√E energy resolution (and low constant term) for η < -2
    ~7%/√E energy resolution for -2<η< 1
    ~10-12%/√E in barrel
  π/K/p separation
    momentum distributions are very η-dependent
      Forward η: up to ~50 GeV/c
      Central η: up to ~4++ GeV/c
      Backward η: up to ~5-6 GeV/c
    suppression factors ~100 required
  Spatial resolution of primary vertex
    ~10-20 μm
  Jets
    HCAL needed at forward η; at mid-η no HCAL needed
There are site-dependent requirements but overall they are rather similar:

## Slide 8: EIC Detector Requirements and R&D in Context
In Short:
  Hermetic detector, low mass inner tracking, good PID (e and π/K/p), calorimetry
  Moderate radiation hardness requirements, low pile-up, low multiplicity
Comparison:
  Majority of R&D in HEP and HENP is currently related to LHC phase-I and phase-II upgrades
  Radiation hardness and rate are top R&D items for pp. Less emphasis on PID (notable exceptions is LHCb). High multiplicity and high data taking rate for AA (ALICE).
  With end of phase-I R&D efforts on MAPS, PID, GEM-TPC will stop
Specific requirements for an EIC demand R&D that is not covered by main stream HEP, HENP R&D - we have to drive it ourselves

## Slide 9: Some Statistics (I)
Note: < 2014 proposals were considered every 1/2 year. Those are added up.
First year: moderate requests in terms of funding
Consortia
LRP
  FY17: Record participation this time (expected)
    8 new proposals, new strong international groups

## Slide 10: Some Statistics (II)
  Total since 2011: $7,721,740
Fiscal Year
  Total funds requested: $2.45M: worst ratio of available/requested funds ~ 0.41
  Need to work on this together with DOE and EIC User Group SC

## Slide 11
EIC R&D
Examples

## Slide 12: eRD1: Calorimeter Consortium
  Goal: Develop simple, cost effective, flexible techniques to build compact sampling calorimeters with good characteristics.
  Efforts:
    Sci-fiber EM calorimeter (SPACAL)
      Compact W-scifi calorimeter, developed at UCLA
      Investigating high resolution version for e-going endcap
    Crystal EMCal
      Option for high resolution e-going endcap calorimeter
    Shashlik EMCal
      Option for h-going endcap calorimeter
    HCal
      Prototype development in collaboration with STAR forward upgrade and sPHENIX
    Sensor
      SiPM and APDs, radiation studies and support electronics
BNL, CALTECH, CUA, JLAB, IUCF, NPN Orsay, PSU, TAMU, UCLA, USTC, YPI

## Slide 13: eRD1: W-SciFi SPACAL - EIC Forward
  Thin fibers embedded in composite absorber
    Two versions ‘O’ (old) and ’S’ (square)
Test Run 2016 FNAL
EIC Barrel EMcal
EIC Forward
Very Bright
SiPM Readout.
    ’S’ version: Achieve target of 7%/√E with constant term ~ 1% constant term at 10°, 2.9% at 4°
  Next: Systematic study of behavior of Si sensors in realistic conditions, R&D on efficient and compact light collection scheme

## Slide 14: eRD1: Crystal Calorimeter
  e-going direction needs high precision calorimetry (few%/√E)
  PbWO4 calorimeter desired for this role, extensively used for high precision calorimetry (CMS, JLab, PANDA…) because of its energy and time resolutions and its radiation hardness
  BTCP (Russia) produced high quality crystals in the past but out of business
  SICCAS (China) problems maintaining good crystal quality
  New potential candidate: CRYTUR, Czech Republic
Goal:
Develop process towards acceptable crystals quality assurance towards EIC needs
Develop an alternate supplier of PbWO4 (CRYTUR) - evaluate quality, work with manufacturers to improve quality

## Slide 15: eRD2: A Magnetic Field Cloaking Device
  Issue: Strong dipole magnets in forward/backward direction affect beam optics.
  Goal: Shield beam pipe and allows beam to tunnel through magnetic fields w/o disturbance of outside fields
SUNY, RIKEN, BNL
  Method: Wrapping layers of layers of AMSC high-temperature superconductor around beam pipe
45 layers → 0.5T
SUNY, RIKEN, BNL
Notes: The results we reported previously predicted that a cylinder made from
45 (10) layers of 46 mm wide AMSC high-temperature superconductor wire
insert at liquid nitrogen (liquid helium) temperature could shield a magnetic
field of 0.5 T.

## Slide 16: eRD2: A Magnetic Field Cloaking Device
  Beam tests in progress:
    BNL, Van de Graaff beam line
    Shield beam from a transverse magnetic field with a 1.3 m SC cylinder at liquid nitrogen temperature
  Coming up:
    High-field shielding test with MRI magnet at ANL
    Shield a 0.5 T field with a 10 cm SC cylinder at liquid nitrogen temperature.
  Producing multi-layer shield
    Successful first soldering and performance test with miniature version of shield
Notes: The results we reported previously predicted that a cylinder made from
45 (10) layers of 46 mm wide AMSC high-temperature superconductor wire
insert at liquid nitrogen (liquid helium) temperature could shield a magnetic
field of 0.5 T.

## Slide 17: EIC R&D: Involving HS Students Successfully in eRD2
Fall 2016: Egleston Research Scholar at Columbia University-Fu Foundation School of Engineering
Semi- finalist:
Ayesha Chhugani
“Most Outstanding Exhibit in Computer Science, Engineering, Physics or Chemistry”

## Slide 18: eRD3: Micro-Pattern EIC Tracking System
  R&D effort focuses on intermediate tracking system
    Barrel tracking system based on MM detectors (Dedicated barrel / curved MM EIC R&D program) manufactured as cylindrical shell elements and
    Forward/Backward tracking system based on triple-GEM detectors manufactured as planar segments (Collaboration with eRD6 FIT/UVA)
  R&D strategy:
    Design and assembly of large cylindrical MM detector elements and large planar triple-GEM detectors
    Test and characterization of MicroMegas and triple-GEM prototype detectors
    Utilization of light-weight materials
    Development and commercial fabrication of various critical detector elements
Temple, Saclay

## Slide 19: eRD3: Micro-Pattern EIC Tracking System
Highlights:
  Substantial facility development at Saclay (Assembly and testing of MM detector) and Temple University (Assembly and testing of GEM detectors) for micro-pattern detectors
  Work on commercial development of various components including GEM foils and 2D readout foils
    Commercialization of GEM foils is issue
  Successful development and application of a dedicated new chip readout system (DREAM chip) for micro-pattern detectors
  Remaining program plans to focus on assembly and testing of larger detector elements using X-ray and cosmic-ray scans using novel assembly techniques

## Slide 20: eRD6: Tracking/PID Consortium
  Existing Since 1st Round of EIC R&D
    Brookhaven National Lab: MiniDrift & TPCC
    Florida Institute of Technology: ZigZag Planar GEMs
    Stony Brook University: RICH & TPCC
    University of Virginia: Stereo-COMPASS Planar GEMs
    Yale University: 2Gem+μMEGA
  Recent Additions
    INFN Trieste: RICH PID
    Weizmann Institute of Science: EIC TPC
  Largest experiment at Fermilab Test Beam Facility with 19 detector stations in single experiment
Sector Test: October 2013
TPC/Cherenkov: April 2016
BNL, FIT, INFN Trieste, SUNY, UV, WIS, Yale

## Slide 21: eRD6: Mini-Drift GEM Tracking Detector
  Triple GEM stack with a small drift region (mini TPC type configuration)
  Position and arrival time of the charge deposited in the drift region were measured on the readout plane allowing reconstruction of track traversing the chamber.
  Minidrift overcomes resolution degradation with incident angle for conventional GEM tracking detectors using only charge centroid information.
  Compatible with all forms of planar GEM tracker.
Normal Chamber
MiniDrift

## Slide 22: eRD6: Cherenkov TPC
  Combines the functions of a TPC for charged particle tracking and a Cherenkov detector for particle identification in same volume
  Prototype:
    TPC: 10cm drift + 10x10cm2 4GEM
    Cherenkov: 3.3x3.3cm2 pad array + 10cmx10cm 4GEM
    Common Gas: CF4 (vdrift = 7.5cm/μs & large N0)
  Successful demonstration of proof of principle - TPCC works!
  Quantified performance specs like track resolution and Cherenkov light yield

## Slide 23: eRD6: ZigZag Strip Readouts
  Goal: Improve common readout boards with more complex zigzag design
  Test with 3GEM readout and X-ray source
  Early results of boards tested at FNAL showed non-linear behavior
  Recent: Scans of PCBs with improved zigzag strip design aiming to reduce non-linear response and achieve <100 μm spatial resolution
  Vastly improved
  Linear response over whole range
  > 95% events fire 2 or 3 strips (before mostly 1)
  Continue work with company to further improve PCBs

## Slide 24: eRD14: PID Consortium
  Particle ID is essential for EIC
  eRD14 is developing a suite of detector systems covering the full angular- and momentum range required for an EIC
    Imaging Cherenkov detectors are the primary technology
e-endcap
h-endcap
barrel
10x100 GeV
Q2 > 1 GeV2
DIRC
Aerogel RICH
Dual-radiator RICH
p/A
e
GeV
rapidity
Current Projects:
  h-side: RICH with two radiators (gas + aerogel) are needed to cover the full momentum range: more than 3 s.d. separation for π/K/p over 3-50 GeV/c
  e-side: Compact aerogel RICH covering up to 10 GeV/c (π/K/p) can provide the required PID and allow for an endcap design optimized for EIC physics requirements
  Barrel:
    DIRC is compact and can cover momenta up to 6-7 GeV/c
    ToF under investigation, still issue with determining T0 and related t-resolution
ACU, ANL, BNL, CUA, William & Mary, Duke, GSU, GSI, Howard, INFN Ferrara, INFN Roma, ISS Rome, JLAB, LANL, ODU, USM, UIC, UNM, SC, Yale

## Slide 25: eRD14: Dual Radiator RICH Detectors
  First dual-radiator RICH developed for use with a solenoidal detector
  Combination of C2F6 gas and n=1.02 aerogel leaves no gaps in coverage
  Outward-reflecting mirrors reduce backgrounds and (UV) scattering in aerogel
  3D focusing reduces photosensor area
  Geant4 simulations show excellent performance for both hadron and lepton ID
Particle separation power for tracks with 15° polar angle

## Slide 26: eRD12: Low Q2-Tagger, Luminosity Monitor & e-Beam Polarimeter
  Successful conclusion of project:
  Initial design and integration into the IR completed
  Optimized the IR design to integrate:
    Luminosity monitor
    Lepton polarimeter
    Low Q2-tagger
  Developed a Monte Carlo code for Bremsstrahlung taking into account the polarization dependence of the Bremsstrahlung cross section
  Integrate a first layout into the EicRoot simulation package
    Develop a dedicated e-polarimeter simulation package
    Determine detector performance requirements based on physics and machine backgrounds
  Targeted Detector R&D which fulfills the determined requirements
BNL

## Slide 27: eRD12: Low Q2-Tagger, Luminosity Monitor & e-Beam Polarimeter
0 m
18 m
-15 m
-35 m
-45 m
hadrons electrons
Lumi Monitor
Integrated into IR
Includes a pair spectrometer
Effect of beam optics studies
Angular divergence dominates the acceptance, current parameters are ok
Low Q2-tagger
Tracking code to calculate scattering angle of electron
Iterate with machine designers to improve IR design
Pythia studies show acceptance down to Q2 O(10-5 GeV2)
Forward Proton Spectrometer
Important for DVCS
Roman Pot integrated into IR
Studied the acceptance of protons through the lattice
Feedback to machine designers to push for next iteration
Electron polarimetry
Identified the space in the tunnel
Estimated constraints on the laser (cathode by cathode measurement in about 2 minutes)

## Slide 28: General Remarks from the Committee
  It is great to see proposals come to a conclusion with a deliverable that is of general value for the EIC development (e.g. eRD12)
  Field is getting more crowded and level of funding will not change in the near future. The protocol for proposal submission will be modified and proposals will have to address different funding levels: 100% +/- 25%.
  Given the severe financial constraints, a guideline of one year of support per postdoc will be implemented; this hopefully will encourage securing matching support by the proponents.
  EIC R&D funding is NOT base funding, but should be considered as supplemental funding to initiate new directions.
  There seems to be a tendency of some of collaborations that have been in existence for a longer time to move in the direction of (value) engineering. The committee feels that it is too early for this (R&D versus PED)

## Slide 29: General Remarks from the Project Coordinator
  It is great and rewarding to see the program grows and mature
  Program has participants from 43 institutions (11 non-US)
  The number of peer reviewed publication grows steadily
  Certainly in the near future funding is not expected to increase stressing the project (and the committee)
  We will make some changes to the proposal format (include different funding levels) and apply new rules (e.g. only support for 1 year/postdoc) to mitigate some funding issues
  Need to work with DOE to implement LRP recommendation and increase funding.
  The program needs to have room (i.e. funds) for further grow