## Slide 1
Detector R&D
Thomas Ullrich, EIC User Meeting
CUA, Washington DC, July 29, 2018
Photos in part from talks at EIC Detector R&D Committee Meeting: July 26/27, 2018, CUA

## Slide 2: Setting the Stage: EIC Detector(s)
Consensus within the EIC community:
  A least 1 general purpose detector
  Needs for a second detector - majority favors a second general purpose detector instead of more specialized detector
  Arguments for 2 detectors similar as for every collider
  The 2 detectors should be complementary (different strengths) - success of combined HERA data is good example
Both machine designs include at least 2 IRs

## Slide 3: General Purpose EIC Detectors
Forward
Backward

## Slide 4: General Purpose EIC Detectors
Forward
Backward
Magnet
  Originally many solutions discussed (Dipole, Toroid, …)
  Focus now on Solenoidal Magnet
  Compact EIC detector requires large fields: B ~ 3T
  Available magnet: BaBar B = 1.5 T
  No ongoing R&D

## Slide 5: General Purpose EIC Detectors
Forward
Backward
Polarization/Luminosity
  Electron Polarization: Compton Process (need 1% or better)
  Proton/Light Ion Polarization: experience from RHIC but tighter requirements at EIC
  Luminosity Measurements
blue = ongoing R&D

## Slide 6: General Purpose EIC Detectors
Forward
Backward
Barrel
  Si-Vertex tracker: low X/X0, resolve charm vertices Þ MAPS, ….
  Main tracker: p, dE/dx Þ TPC, Si-Tracker, GEM, MMG, μRWELL, …
  Particle ID (PID): p < 10 GeV Þ DIRC, EMCal, …
  EM Calorimetry: e/h, g, p0, …
  Hadron Calorimetry: jets (neutral component) Þ optional
  Muon Detector: vector mesons Þ optional
blue = ongoing R&D

## Slide 7: General Purpose EIC Detectors
Forward
Backward
Forward
  Si-Vertex tracker: resolve charm vertices Þ MAPS, ….
  Tracker: p Þ GEM, MMG, μRwell, …
  Particle ID (PID): p < 50 GeV Þ RICH, TRD, …
  EM Calorimetry: E, e/h, g, p0, …
  Hadron Calorimetry: E, e/h, jets Þ high resolution needed

## Slide 8: General Purpose EIC Detectors
Forward
Backward
Very Forward
  Nuclear Breakup/Fragments: ZDC, Roman Pots, Forward proton detector
  Proton pT, t measurement: Roman Pots

## Slide 9: General Purpose EIC Detectors
Forward
Backward
Backward
  Si-Vertex tracker
  Tracker: p Þ GEM, MMG, μRwell, …
  Particle ID (PID): Þ RICH, EMCal
  EM Calorimetry: E, e/h Þ high resolution needed

## Slide 10: General Purpose EIC Detectors
Forward
Backward
Very Backward
  Access to low Q2 region: Low Q2 tracker

## Slide 11: R&D Driver: Requirements
Big View:
  Hermetic detector, low mass inner tracking
  good PID (e and π/K/p)
    extreme requirements in forward region
  Good calorimetry
    HCAL: extreme req. in forward region
    EMCAL: extreme req. backwards region
  Moderate radiation hardness requirements, low pile-up, low multiplicity
From R&D Handbook (later more)
p (GeV/c)
From WP
Hard Numbers:
  General consensus on many fronts but need more refinement
  Identify physics driver and specify/verify needs
  Also need to take into account correlation between subsystems
eRD1: Tanja Horn
Within the next year we need to refine detector requirements from detailed simulations focusing on main physics driver

## Slide 12: Generic EIC Detector R&D Efforts
Generic EIC Detector R&D Program (covered here)
Other substantial efforts with impact on EIC
  Laboratory Directed Research & Development Programs (LDRDs) at National Labs in the US (BNL, JLAB, ANL)
  CERN
    R&D program with partial match with EIC needs (e.g. RD51 Micro-Pattern Gas Detectors Technologies)
    LHC Experiments R&D for phase-I upgrades, especially ALICE (TPC, ITS, SAMPA) and LHCb (RICH, trigger less DAQ). Now in production, R&D finished.
  R&D at Belle-II and Panda (crystals, DIRC, …)
  ILC related R&D
Notes: DIRC = Detection of Internally Reflected Cherenkov light

## Slide 13: Generic EIC Detector R&D Program
Started 2011 BNL, in association with JLab and the DOE Office of NP
Funded by DOE through RHIC operations funds
Program explicitly open to international participation
Standing EIC Detector Advisory Committee consisting of internationally recognized experts in detector technology
Meets twice a year, funding limited to one year (FY)
  ~January: Review of ongoing projects
  ~July: Review and new proposals
Current: Marcel Demarteau** (ANL), Carl Haber (LBNL), Peter Krizan (Ljubljana),
Ian Shipsey (Oxford), Rick Van Berg (UPenn), Jerry Va’vra (SLAC), Glenn Young (JLab)
Retired:
Robert Klanner (Hamburg),
Howard Wieman (LBL)
**Chair
URL: https://wiki.bnl.gov/conferences/index.php/EIC_R%25D

## Slide 14: R&D Program In Numbers
Chart: Number of Proposals per FY
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Number of Proposals | 13 | 7 | 6 | 12 | 13 | 17 | 18 | 11
  Typical 10-11 projects supported
  Attempt to merge projects in consortia when related
  Participation:
    46 institutions (13 non-US)
    6 Natl. Labs
    187 participants
  Since 2016 budget flat ~$1M
  Requested funds exceed available funds by factor 1.5-2.5
Chart: Funding per FY
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Number of Proposals | 568000 | 1183000 | 798000 | 1489000 | 1113000 | 1000000 | 1000000 | 1000000 | 1000000
LRP
N.B.: Generic RHIC detector funding was $4M in 2018$

## Slide 15: FY19 Projects
11 Projects are considered in FY19
  eRD1 - Calorimeter consortium
  eRD6 - Tracking/PID consortium
  eRD14 - PID consortium
  eRD22 - GEM Transition Radiation Detector (TRD)
  eRD16 - Fwd Silicon tracking
  eRD18 - Central Si tracking/Si sensors
  eRD15 - Compton spectrometer
  eRD17 - e+A Simulations/Nuclear Breakup (BEAGLE)
  eRD20 - Software consortium
  eRD21 - Background studies
  New - DAQ/Streaming Readout
Green = consortia
Notes: Project Engineering and Design

## Slide 16: W-SciFi Calorimetry (eRD1)
Scintillating fibers embedded in W-powder composite absorber
Development led to working prototypes with good energy & position resolutions, choice of readout technology, all coupled with levels of radiation hardness that would result in a capable EM calorimeter for the barrel and hadron-going directions at an EIC.
Technology is used for EMCal in sPHENIX
Issue: In RHIC beam in 2017, η=3.75, ~1011 n/cm2 SiPM show non-homogeneous degradations Þ need for a good monitoring system for a W-SciFi calorimeter (future project?)
UCLA/BNL/IU/PSU/TAMU

## Slide 17: Hadron Calorimetry (eRD1)
New effort: examine timing of signals from a hadronic calorimeter to possibly dramatically (factor 2) improve energy resolution
Utilization of observable correlated with the total number of neutrons in the shower to make correction to the observed total energy on the event-by-event basis.
  Ratio of Cherenkov to Scintillation light in DREAM
  Timing information of shower development may be used in a similar fashion.
  In addition: ZEUS FNC Tile/WLS method to use timing for e/h separation
FY19: proof of principle using a small, 3x3 prototype (iron and lead absorber and scintillation tiles) in FNAL test beam
Had
EM
UCLA/BNL/IU/PSU/TAMU
Notes: Figure 5 shows scatter plot showing ratios of Cherenkov-to-Scintillation for 50 GeV
pions, and ratio of energy deposited in the first 1.25 ns to the total energy deposited in
the calorimeter, as predicted by MC (IEEE Transaction on Nuclear Science, Vol.63,,
No2, April 2016, A. Benaglia et al.). In both cases, a reliable correction to the total
energy is possible on event-by-event basis.

## Slide 18: Scintillating Glasses (eRD1)
e-going direction needs high precision calorimetry (≲ 2%/√E)
Requires Lead Tungstate (PbWO4) crystals
  Despite progress still a struggle to work with vendors (SICCAS & CRYTUR) to get high quality PbWO4 crystals
New effort: Study various scintillating glasses
  Similar to lead glass in many properties but exhibit up to 100x the light yield per GeV.
  Path to inexpensive high resolution EM calorimeters
Past: Limited to small samples due to difficulties with scaling up the production while maintaining the needed purity.
The VSL at CUA offers the facilities and expertise
Samples made at CUA/VSL with new method. 35 times lighoutput of PbWO4
IPN-Orsay, CUA,
VSL, Caltech
Notes: Vitreous State Laboratory (VSL).

## Slide 19: GEM R&D Program (eRD3)
Effort concentrated on forward GEM and barrel MMG tracking solutions
Large, well equipped, laboratory has been created at Temple University partly from this program but with significant help from the University.
The laboratory now includes optical CCD-based scanners for large GEM foils, ultrasonic baths, and an X-ray characterization station
Real resource for the MPGD community
  Analyzed foils for BONUS experiment and Mecaro (Korean company).
Characterization with cosmics and x-rays of triple-GEM detector with Kapton spacer rings and G10 spacer grids closes out the eRD3 program.
Temple, Saclay

## Slide 20: Large, Low-Mass Prototype GEMs (eRD6)
Initial assembly of carbon-fiber frame prototype and test
Encouraging:
  CF frame doesn’t show any large deformation when stack is tensioned
  No issues with conductivity of CF
  Total chamber mass below 3 kg (w/ HV filter but w/o FE electronics)
  First data: Readout uses long zigzag strips, find low noise
Problematic:
  Detector did not hold full voltage (HV trips) probably caused by on parts by insufficient stretching of the 5 foils in the stack
Remedies:
  Redesign and improvement of inner frames and pull outs
  FY19: pull-outs with a more solid design (PolyEther Ether Ketone)
FIT
Notes: PEEK Polyether ether ketone

## Slide 21: R&D on MPGDs for RICH Detectors
Gaseous single-photon detection with MPGDs for high-momentum RICH
  Development of resistive MMG prototype with miniaturized pad-size
  Use of innovative photocathode based on NanoDiamond (ND) particles coupled to MMG
Near future:
    Beam test with MMG + ND
    Production of a new set of small-size THGEM coated with ND and hydrogenated ND (HND)
INFN
Trieste
Notes: High pt -> gas RICH

## Slide 22: μRWELL Detectors (eRD6)
Resistive micro-well detector (μRWELL) detector
  HV drift cathode, a drift gap, and a micro-well layer (similar to a single GEM foil) which is mounted on a resistive readout board
  Combines the advantages of both GEM and Micromega MMGs, needs no stretching
Goal: cylindrical μRWELL layers (possible part of main tracker)
Acquired and assembled one small 10 cm × 10 cm prototype with 2D X-Y strips readout
  X-Y strips signal are shared through capacitive coupling
  Analysis of the data just started and is ongoing
FIT, UVA, Temple

## Slide 23: Particle ID with RICH Detectors (eRD14)
Developing a suite systems covering the full angular- and momentum range required Imaging Cherenkov detectors are the primary technology
Current Projects
  DIRC: 10 GeV/c for p/K, 6 GeV/c for π/K, and 1.8 GeV/c for e/π
    Focus on lens: radiation hardness test & realization of 3-layer lenses with improved radiation hardness using PbF2 and sapphire.
    Preparation for transfer of PANDA DIRC prototype to the US.
Notes: In a DIRC (Detection of Internally Reflected Cherenkov light), another design of a RICH detector, light that is captured by total internal reflection inside the solid radiator reaches the light sensors at the detector perimeter, the precise rectangular cross section of the radiator preserving the angular information of the Cherenkov light cone.

## Slide 24: Particle ID with RICH Detectors (eRD14)
  dRICH: RICH with two radiators (gas + aerogel) to cover the full momentum range: more than 3 s.d. separation for π/K/p over 3-50 GeV/c in forward region (up to 15 GeV for e/π)
    Focus on simulations
    FY19: Build small prototype (with INFN support)
  mRHIC: Compact aerogel RICH covering up to 10 GeV/c (π/K/p)
    First RICH with (Fresnel) lens focusing
    Test beam data taken in June/July 2018
    FY19: Use mRICH to work on integrated readout sensor electronics solution for all Cherenkov systems
    Beam test at Fermilab 6/2018
Institutes: ACU, ANL, BNL, CUA, William & Mary, Duke, GSU, GSI, Howard, INFN Ferrara, INFN Roma, ISS Rome, JLAB, LANL, ODU, USM, UIC, UNM, SC, Yale
Notes: In a DIRC (Detection of Internally Reflected Cherenkov light), another design of a RICH detector, light that is captured by total internal reflection inside the solid radiator reaches the light sensors at the detector perimeter, the precise rectangular cross section of the radiator preserving the angular information of the Cherenkov light cone.

## Slide 25: Something to Worry About
Photon Detectors: The most important challenge is to provide a reliable highly-pixilated photodetector working at 2-3 Tesla. This problem is not yet solved.
  SiPMTs: in the past rejected for RICH detectors because of the neutron damage. This needs dedicated studies.
  MCP-PMTs: As far as MCP-PMTs, we do not know if the present MCPs are even designed right for the 2-3 Tesla operation. Needs studies.
  Large-Area Picosecond PhotoDetector (LAPPD)
    Commercialized by INCOM after initial development by LAPPD collaboration
    Promising but still not fully applicable for EIC needs. Work is needed on improving LAPPD’s in strong fields while maintaining QE and resolution. This is a major action item.
See also talk by S.Dalla Torro on Sunday
Notes: Large-Area Picosecond PhotoDetector (LAPPD)

## Slide 26: Forward/backward Silicon Tracking (eRD16)
Aim: Conceptual design of Si-tracker for forward/backward scattering angles
  Science-driven sensor specifications
  Optimized disk geometry and layout
  Conceptual arrangement of services,
  Optimized integration with inner Si-tracker,
Close collaboration with eRD18 (barrel Si-tracker)
LBL

## Slide 27: Central Si Tracking and Vertexing (eRD18)
Aim: Conceptual design based on depleted MAPS
Sensor development
  Selected technology: TowerJazz 180 nm modified process
    Fully depleted with small collection electrode
    Prototype test structures evaluated
    Drafted preliminary EIC DMAPS specifications
    Considering a timing layer with faster readout to tag bunch crossings
Layout simulations / detector performance
W. Snoeys, NIMA 871 (2017) 90–96
m @ 1 GeV/c
20 x 20 mm2 pixels
Birmingham

## Slide 28: FY19: Si Tracker Efforts (eRD16&18)
Sensor development
  CERN-TJ Investigator 2 chip
  ATLAS MALTA chip
  Additional designs will be available in fall
    Work with chip designer at RAL
    Simulate possible readout architectures
    Explore tradeoff between power and pixel size
Explore interface of barrel with forward/backward disks
Study trade-offs between barrel lengths and disk radii
Explore low-mass mechanical support concept(s) and cooling
Perform initial set of fast and slow simulations towards an all-Si tracker

## Slide 29: Background Studies (eRD21)
Background Studies and the impact on the IR and Detector design/operation, electronics, beamline components
  Synchrotron radiation, beam-gas interactions, beam halo effects and beam losses, neutron flux, …
Substantial progress in FY18 created and benchmarked realistic simulation tools and techniques with a validation procedure using the HERA configuration
  Applied this work to current JLEIC configuration (realistic machine configuration, vacuum pipe geometry and materials) to produce the first results of background due to synchrotron radiation.
  Developed tools and procedures of general applicability to any EIC design
BNL team have now joined eRD21.
JLAB, SLAC, UCONN, ODU, BNL

## Slide 30: Take Away Message
Despite not having a concrete detector design created by established collaborations the subsystems needed are rather well defined although choice of technology is still open in many places
Requirements are approximately known but need to be refined further
The EIC R&D program is a vital part of the EIC efforts with many active participants
Despite being underfunded the projects make steady and excellent progress. Publication record is very good.
For the first time in 4 years the number of proposals is dropping
Big challenges in PID (see next talk by Elke) that need our full attention. LAPPDs are of great importance.

## Slide 31: Project: EIC Detector Handbook
“Living” document on detector requirements, R&D needs, available technologies, EIC kinematics and more
Should be (once released) regularly updated as requirement get refined
  Needs user input - don’t complain, write and add to it or change and improve
Received lots of input from members of eRD1, eRD6, eRD14, eRD18, eRD22
Editors (A. Kiselev, TU) now integrating text, ref., figures, iterating with authors
Currently 53 pages and growing
Missing: Trigger and DAQ, parts of pol. measurement, hadronic calorimeter
Plan first release in August (yes 2018)

## Slide 32
Backup Slides

## Slide 33: Definitions
Generic EIC Detector R&D
  R&D that focuses on the need for any EIC detector
  Independent of any specific design that might or might not features a subsystem with that technology
  Needs clear motivation that it is targeted on EIC needs
  Performed by anyone in and outside US
  Little/No Preconstruction Engineering & Design (PED) supported
Targeted EIC Detector R&D
  R&D that focuses on the need for a specific EIC detector
  Collaboration in place and mature detector design exist
  R&D is mostly conducted by collaboration members
  PED is included at some level

## Slide 34: eRD15 Compton electron detector R&D
gc
e- beam from IP
Compton electron
tracking detector
Compton photon
calorimeter
Photons from IP
e- beam to spin rotator
  Compton polarization through Compton backscattering, study of electron detection
  few planes of strips to determine electron momentum from magnet deflection
  1% or better electron polarization measurement
  Best measurement Compton electron detector at SLD ( ~0.5%)
  looking at Roman Pot option on electron side for detector protection, cooling and access
  Status
    Event generator and polarization analysis code package done
    Background from Brehmstrahlung, Interaction Point and halo under control : 10 W laser power CW seems adequate
    Preliminary Wakefield study shows detector can be operated with JLEIC beam structure at 3A
    Roman pot windows still allows measurement at 1% level
Green laser
TOTEM Roman Pot
Hall C Compton
diamond detector
Electron detector not in direct view of synchrotron fan

## Slide 35: R&D plans
incorporate TOTEM Roman Pot design into EIC detector lattice
preliminary pipe, chamber and vacuum design and beam induced background using Molflow
optimization of shielding and geometry to minimize Wakefield
beam test to validate simulation
optimization of electronics and detector for potential bunch by bunch measurement ( if needed )
study and improvement of systematics of measurement for better than 1% measurent

## Slide 36
ESC goals and focus
reach out to the EIC community
communicate present status of EIC software
bring existing EIC software to the end users
produce publicly available consensus-based documents on critical subjects
provide vision for the future
continue work on common interfaces (e.g., geometry, file formats, tracking)
explore new avenues of software development (e.g., machine learning)
EIC Software Consortium (ESC)
ANL, BNL, FNAL, JLAB, SLAC, Trieste, W&M

## Slide 37
ESC status and plans
Considerable progress in FY18
Reach out to the EIC community
Bring existing EIC software to the end users
Play active role in software-related workshop organization
Gain missing knowledge and apply it to practical tasks
Arrange expert discussions and come to a consensus-based decisions
Take measures to prevent future EIC software divergence
Try to establish forward looking vision of EIC software
Work closely with EICUG Software Working Group
FY19 goals
Development of Detector Simulations
Geant4 Simulations physics list, validation
Interfaces and integration “software sandbox”, event data model (ProIO)
ESC Initiatives Containers, Machine learning, Monte Carlo Event Generators

## Slide 38: eRD22: GEM based Transition radiation detector/tracker for EIC
Yulia Furletova(JLAB)
on behalf of GEM-TRD/T working group
Notes: Title Page

## Slide 39
Electron identification (e/hadron separation)
J/Ψ, φ
Br (J/->e+e- ) ~6%
Br (J/->+- ) ~6%
GPD and
Coherent Exclusive Diffraction
(saturation)
b
c
W
e
Br (B->e++XC ) ~10%
Heavy quark tagging
Br (D->e+X ) ~16%
Exotic spectroscopy (pentaquarks, tetraquarks, XYZ)
Other BSM physics
Saturation
Coherent Exclusive Diffraction
b
e
е’’
Ivan Vitev
Notes: Interior Page Design 2

## Slide 40
eRD22 GEM-TRD/T
TEAM:
Jefferson Lab: Howard Fenker, Yulia Furletova, Sergey Furletov, Lubomir Pentchev, Beni Zihlmann , Chris Stanislav, Fernando Barbosa
University of Virginia: Kondo Gnanvo , Nilanga K. Liyanage
Temple University: Matt Posik , Bernd Surrow
Goal:
To develop a next generation of transition radiation detectors to improve electron identification (e/hadron separation) at EIC
Critical issues/solutions of TRD operation:
High occupancy in Forward region -> need to find a replacement for straw or wire chamber => use a high granularity offered by GEM technology
Wire Chambers: Space charge suppress late signals => use GEM technology
need cluster separation in time =>
Use GEM technology combined with fADCs
- Optimization of entrance window (and for multi-layered TRD also an exit window) for TR-photon
Notes: Interior Page Design 2

## Slide 41: Test Setup at JLAB HALL-D
Yulia Furletova
3-6 GeV electrons in Hall-D from pair spectrometer
We performed a GEANT4 simulation of TRD setup with GEM detector (gas and radiator volumes) for a single layer operation and estimated e/pi rejection factor.
We built and tested a new GEM based TRD prototype and optimized its performance (new HV divider, different drift filed voltages, gas gain, etc)
Front-end electronic / DAQ :
  Test new DAQ with Flash ADCs
We performed a test beam measurements using the existing facility at JLAB Hall-D
Test of different TR-radiators
New gas-mixing system is ready to use.
Electron beam only => cover ½ of the sensitive area with radiator to “mimic” pion response
Notes: Interior Page Design 2

## Slide 42
Yulia Furletova
Distance in gas [mm]
GEM TRD/T Energy deposition (dE/dx + TR) vs distance
R:5cm,
D: 2,3,4cm
Xe/CO2 (80/20)
e,
~3 GeV
dE/dx for Pions
 | 90% eff | 70% eff
2cm Xe | 2.5 | 12
4cm Xe | 4.5 | 17
MC simulation: Very preliminary rejection, single module (likelihood method)
Reg. follies radiator
GEANT4 simulation
Measured data
Slope in dE/dx, possible problems:
  Bad gas mixture
  Wrong HV settings
  Diffusion
  Space charge
Clearly see TR-photons
dE/dx + TR for electrons
Notes: Interior Page Design 2

## Slide 43: Proposal for FY19
In addition (budget request fro FY19)
We have identified a several issues and studies which should be pursued in addition to those in our original plans as important steps towards the realization of a new generation of transition radiation detectors as a part of the EIC project.
Gas system: gas analyzer to begin quantifying and monitoring contaminations and to measure the concentrations of the Xe and CO2 gasses
( split a cost with Hall-D) ca. $7k (40%)
In collaboration with readout consortium:
  On-line particle identification: to move a part of an off-line reconstruction software into on-line (FPGA evaluation board ~$7k)
  Readout hardware: find a cheaper solution/replacement of FlashADC125 ($50/channel -> 5-7$/channel)
Detector prototype: following the EIC R&D (tracking consortium eRD6) effort on new technology such as RWELL detectors, we are planning to work in parallel with the consortium toward an optimization of the detector for TRD/Tracking application. ($15k)
Tracking: evaluate the performance of our prototype as a tracker (no cost)
Radiator optimization: we need to identify and test promising new radiator materials to optimize the yield of TR-photons.
Yulia Furletova
6
CEA-Saclay has an interest in ASIC developments for EIC and in particular for GEM-TRD/T. We are looking forward to collaborate!
Notes: Interior Page Design 2

## Slide 46: Summary and Future Plans for eRD1
  Status of current projects
  W/SciFi calorimeter R&D
    Early R&D lead to full implementation into sPHENIX detector
    Now investigating alternative readout with WLS bars
    Radiation damage studies of SiPMs is ongoing
  W/Shashlik calorimetry
    Investigating as a possible alternative to W/SciFi calorimetry
  Hadron Calorimetry
    Investigating dual readout HCAL measuring time development of hadronic shower
  Crystal Calorimetry
    Study of PWO crystals is ongoing; continuing to investigate crystals from two possible vendors
    New investigation of scintillating glass materials is beginning
  Investigating other forms of calorimetry
    Particle flow, radiation hard, luminosity monitors, …

## Slide 47: Future Plans
Radiation Damage Studies with SiPMs
New SiPMs may perform better under irradiation
Hamamatsu
KETEK
W/SciFi readout with WLS bars
W/Shashlik Calorimetry with SiPM readout of individual fibers
Measuring time development of hadronic showers
Dual Readout Hadronic Calorimetry
PWO crystals from SICCAS
CUA/VSL scintillating glass
Bubbles
Material/ Parameter | PbWO4 | CUA/VSL glass
Luminescence (nm) | 420 | 440
Relative light output (compared to PbWO4) | 1 | 11-35

## Slide 48
eRD14 – overview
Dual-radiator RICH (dRICH).
First dRICH for solenoid detector
Aerogel & C2F6 gas provide continuous coverage up to:
60 GeV (p/K); 15 GeV (e/p)
1
Compact modular aerogel RICH (mRICH)
First RICH with (Fresnel) lens focusing
Small, sharp ring improves performance and reduces photosensor area (cost)
Covers up to 8 GeV (p/K) and 2 GeV (e/p)
Next-generation barrel DIRC
First DIRC with high-resolution in x,y, and t
3D reconstruction allows leap in performance
Radiation-hard optics being developed
Covers up to 6 GeV (p/K) and 2 GeV (e/p)
Photosensors and electronics
Large area low-cost LAPPD (MCP-PMT) photosensors
Sampling electronics (GHz) for small-pixel detectors
6 GeV